## Slide 1: Space Weather Discussion
David A. Vallado* and Sarthak Srivastava**
*Center for Space Standards and Innovation COMSPOC, **Ansys Corp
October 18, 2023

## Slide 2: Overview
Overall COMSPOC needs from SPW
  Products
  Timelines
ODTK Plugin for WAM

## Slide 3: Overall Needs
Produce highest quality ephemerides
  Conjunction calculations of O/O vs secondaries
Requires accurate atmospheric models and Space Weather indices
Prediction is most important
  Generally ~7 days
  Time required for:
    Accurate solutions to be obtained
      Additional observations to be taken
    Decisions to be made
    Up-link of commanded maneuvers (if needed) to be made
    Maneuver to take effect and move satellite out of the way

## Slide 4: Specific Products
Most traditional atmospheric models require
  NRLMSISE-00, DTM-12, J71, JR-71, etc.
  Solar Flux, F10.7
  Geomagnetic indices
Density\density corrections are also acceptable
  WAM
  Other

## Slide 5: Timing
Need continuous file of data to support
  Like Celestrak
    http://celestrak.org/SpaceData/
  Past operations (calibration etc)
  Current status (where is the satellite now?)
  Future locations
    Most important as predicted conjunctions must be accurate and avoided if necessary

## Slide 6: Results
Initial Plugin developed for STK/ODTK
  (Sarthak Srivastava of Ansys)
  Upload density data files
  Interpolate to get the density at an altitude
  Return the density for use in orbital propagation

## Slide 7: Geomagnetic Storm case: 23-26 March, 2023
Stormy conditions:
Kp ~ 8
Dst ~ -150 nT
Opportunity to study density differences in orbit propagation
Precise estimates of real trajectory available from Satellite Laser Ranging of calibration satellites
LARETS
STELLA/ STARLETTE
(https://space.skyrocket.de/)

## Slide 8: Orbit Propagation error for LARETS (~700 km)
Orbit propagation with STK HPOP for 6 days
Propagation using WAM-IPE density (~5 km) seen to match SLR data much better than other models (~40 km error)

## Slide 9: Orbit Propagation error for STELLA (~800 km)
Orbit propagation with STK HPOP for 6 days
Propagation using WAM-IPE density (~1 km) seen to match SLR data much better than other models (~8 km error)

## Slide 10: Orbit Propagation error for STARLETTE (~1000 km)
Orbit propagation with STK HPOP for 6 days
Propagation using WAM-IPE density (~0.5 km) seen to match SLR data much better than other models (~2.5 km error)